Aircraft:	ANDREWKARMY RV-9A	(Van’s RV-9A)

Serial Number:	90374		  Registration Number:	N169AK

Aircraft Owner:	Andrew Karmy

Date of Inspection:			  Location of Inspection:	1S0

| Total Airframe Hours: |  |
| --- | --- |
| Total Engine Hours: |  |
| Total Propeller Hours: |  |

Inspection Performed By:				 Certificate:

### Preparation — Inspection Consumables

| Oil | 7 qts AeroShell 100WPlus |
| --- | --- |
| Oil filter | Champion CH48110 |
| Spark plugs | 8 - Unison UREM37BY |
| ELT batteries | 8 - Duracell MN1300 alkaline D-cell (every 2 years) |
| ELT remote battery | 1 - Duracell DL 1/3 NB lithium (every 8 years) |
| Air filter recharge kit | K&N 99-5000 |
| Brakes | Brake lining replacement kit |
| Tires/tubes – main | 2 - 5:00x5-6 ply, as needed |
| Tire/Tube – nose | 1 – 4:00x5 shinn, as needed |
| Wheel bearing grease | Hi-temp disc brake grease or Aeroshell 5 |
| Gasket lube | Dow DC-4 |
| Light lubricant | LPS-2 or comparable light lubricant for rod end bearings |

### Time-limited items

| Item | Last change | Next due |
| --- | --- | --- |
| ELT batteries (replace every 2 years) | Feb 2003 | Feb 2005 |
| ELT remote battery (replace every 8 years) | Feb 2003 | Feb 2011 |
| Altitude encoder & transponder certification | Feb 2003 | Feb 2005 |

### Empennage & Fuselage Group

Remove empennage fairing, fuselage inspection & baggage wall covers

Inspect vertical and horizontal stabilizer spar attach points

Inspect elevator horns and attachments, and rear fuselage bulkhead interior

Inspect all empennage structures for corrosion and condition

Inspect all empennage attach bearings for condition/security, lubricate

Inspect rudder control stops and cable attachments for security and cotter pin, rudder light wire for chafing

Inspect elevator trim tab, arm, and actuator rod

Inspect static ports, verify clear

Inspect rear fuselage interior: check skin/bulkheads for cracking, damage, or corrosion, inspect all wiring & plumbing, clean as necessary

Inspect midship elevator bellcrank assembly, lubricate rod end bearings

Re-install rear baggage panels, rear fuse inspection plates, empennage fairing

### Landing Gear Group

Remove nose wheel and nose wheel yoke, clean all parts, and assess wheel bearings, yoke bearings, and tire

Clean & oil yoke bushing, re-install yoke and wheel replacing wheel and/or bearings as necessary

Inspect nose wheel steering mechanism for breakout force and proper movement

Re-install nose wheel, replace as necessary

Remove wheel pants, upper & lower intersection fairings

Inspect wheel pants and fairings for cracks, wear, loose or missing fasteners

Jack plane one wheel at a time using jack adapter in wheel axle

Remove brake assemblies and wheels one at a time

Inspect tires for wear and cracks, rotate if indicated, replace if necessary

Check brake cylinders for condition/leaks, brake lines for security and chafing, inspect brake linings for wear and condition, replace as necessary

Re-pack wheel bearings (hi-temp disc brake grease) every other year

Rotate or replace tires as necessary

Clean and re-mount wheels and brake assemblies including cotter pin

Check/set tire air pressure: 28-34 psi

Clean wheel pants and re-install

Inspect gear/fuselage attach bolts for security and tightness

Inspect fuel vent ports for security and condition

Re-install upper & lower intersection fairings, wheel pants

### Wing Group

Remove wing inspection plates

Inspect entire wing structure internally for cracks and corrosion including fuel tank attach bolts, special attention to main spar

Inspect aileron control mechanism (push tubes, rod end bearings, bellcrank) for condition/security, lubricate rod end bearings

Inspect wing root area including electrical connections and plumbing

Inspect fuel cap and O ring condition

Inspect aileron attach bolts/brackets for security, aileron control stops for security, lubricate rod end bearings

Inspect pitot tube and plumbing for security and blockage

Extend flaps, inspect flap actuator rods and attachment points for operation and security, lubricate rod end bearings

Inspect strobe/nav lights for security and operation

Inspect landing lights for security and operation

Reinstall inspection plates and wing root fairings

### Cabin Group

Remove flap motor cover, inspect flap motor mechanism & wiring for damage and proper operation, lubricate rod end bearing

Remove seat pans for control inspection

Inspect flight controls, lubricate rod end bearings

Inspect condition of seat harnesses, mounts, and attachments

Inspect gear tower area including spar bolts, antennas, wing wiring connections, leaks or chafing

Inspect front-cabin console area including: fuel selector valve, fittings, fuel lines

Check general condition under panel for loose wires, chafing, etc.

Check all avionics and instruments for mounting security

Check cabin heater and controls

Check rudder pedals and brake cylinders for operation and leaks

Remove and inspect under forward wiring tunnel for leaks and chafing

Inspect cabin side of firewall area: aux fuel pump, firewall penetrations, wire bundles, fuel lines, vent tubes

Inspect canopy structure and mechanism for security and wear

Inspect canopy and windshield for cracks

Check fire extinguisher condition

Verify spare fuses available in rear seat pockets

Re-install interior floor panels, seats, flap covers, and seat cushions

Check/change ELT batteries, verify operation, set to “armed”

### Propeller Group

Remove spinner noting orientation for replacement

Inspect spinner and backplate for cracks or damage

Inspect prop hub for cracks or leaks

Inspect crankcase nose seal for oil leaks

Inspect propeller blades for nicks, cracks and/or surface erosion

Re-install spinner

### Engine Group

Service items:

Remove engine cowl

Clean cowling interior and inspect for cracks, distortion, loose or missing fasteners, heat damage

Drain engine oil, collect oil sample for analysis, remove spin-on oil filter, replace and safety wire, refill engine oil per lubrication chart

Cut open oil filter, inspect for particles

Remove plugs noting current installed location

Inspect spark plug condition, clean, re-gap to .016-.022”

Perform leakdown compression test, note compression:

#1		 #2		 #3		 #4

Check magneto timing & Electroair ignition condition and operation

Reinstall spark plugs rotating top to bottom, apply anti-seize paste, torque to 400 in.lbs.

Remove carburetor air box and carburetor heat attachments

Service K&N air filter element every other year

Reinstall air box and all attachments

Remove and clean gascolator screen and bowl

Remove and clean carburetor inlet strainer

Inspect carburetor mounting nuts for security

Check engine controls for proper movement and security

Check exhaust system and mounting brackets for cracks

Re-torque exhaust mounting nuts

Inspection items:

Inspect accessories on rear engine case for security and leaks including: oil temp sender, oil pressure sender, magnetos, fuel pump, vacuum pump pad, oil lines & fittings, crankcase breather

Inspect oil cooler condition including fins for damage or blocking, lines for leaks and/or chafing

Inspect ignition harness, springs and insulators for condition

Inspect starter: pinion & ring gears, mounts, wiring connections

Inspect alternator: mounts, lead connections, belt condition and tension

Inspect plenum/baffle for damage and air leaks

Inspect engine mount system for damage and attachment security

Inspect all firewall penetration seals

Inspect fuel lines for condition, chafing, and signs of leaks

Inspect all wire bundles for security and chafing

Inspect all lines, hoses, and clamps for leaks, improper condition, looseness, and chafing

### Operational Inspection

Verify all inspection panels and fairings secure

Brake system check

Test run engine:

Check oil pressure/temperature within limits

Check aux fuel pump for proper fuel pressure

Check ignition switch, both magnetos grounded check

Check alternator shut off operation

Check fuel gauges for operation

Check static run up

Magneto check

Check for proper idle RPM

Check RPM rise upon leaning mixture (idle mixture)

Check fuel selector for engine shutoff

After shutdown:

Inspect fwf area for fuel, oil, and hydraulic systems for leaks

Re-install cowling

### Documentation

Verify equipment list up to date

Verify Registration, Airworthiness Certificate, and Operating Limitations are current and in aircraft

Verify external data plate secure and installed

Verify EXPERIMENTAL placard installed in cockpit

Verify PASSENGER WARNING placard installed in cockpit

Verify cockpit checklists and Pilot’s Operating Handbook in aircraft

Review Airworthiness Directives for applicability and compliance

Review Service Bulletins/Letters for compliance

Check altitude encoder & transponder certification (every 24 months)

Document Condition Inspection and record maintenance performed in airframe and engine logs

NOTES: